## Slide 1: Circuits CMSC250

## Slide 2: Announcements / Reminders / Schedule
Recording of Sunday’s review session is up.
Homework 4 solutions are also up.
  Consult them if you have questions about combinatorial proof structure, or other questions!
Remember:
  No hw this week
  No quiz this week
  But next week there will be both! 
Today & Thursday: circuits!

## Slide 3: Announcements / Reminders / Schedule
Expectation of grading:
  Homework 4 grading comes first, by Monday.
  Midterm grading will take extra time (Friday 03-12).
  You will have a full week (through Friday 03-19, Springbreak Friday) to submit regrade requests on Gradescope.
Midterm solutions posted as soon as Thursday 08:01 AM
  Probably a bit later, to avoid last – minute panic of any kind.
Logic behind solving will be covered in one of the two discussion sessions next week.

## Slide 4: Circuits
We can build circuits for addition, multiplication, division, bit shifting…
Every logical operation we have learned maps straightforwardly to a tiny piece of hardware called a logical gate.
These gates connect to each other to make arbitrarily complicated circuits!

## Slide 5: From a truth table to a formula
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 6: From a truth table to a formula
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
Let us focus entirely on the rows that output 1!

## Slide 7: Focusing on the 1st row…
p | q | r | output
0 | 0 | 0 | 1
Write a simple formula that is ’1’ only on inputs p =0, q = 0, r = 0.
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 8: Focusing on the 1st row…
p | q | r | output
0 | 0 | 0 | 1
Write a simple formula that is ’1’ only on inputs p =0, q = 0, r = 0.
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 9: Focusing on the 4th row…
p | q | r | output
0 | 1 | 1 | 1
Same deal
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 10: Focusing on the 4th row…
p | q | r | output
0 | 1 | 1 | 1
Same deal
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 11: Focusing on the 5th row…
p | q | r | output
1 | 0 | 0 | 1
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 12: Focusing on the 8th row…
p | q | r | output
1 | 1 | 1 | 1
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 13: How do we combine those simple formulae?

## Slide 14: How do we combine those simple formulae?
Outputs 1 if and only if the truth table outputs 1!
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 15: How do we combine those simple formulae?
Outputs 1 if and only if the truth table outputs 1!
We want to do this in hardware!
p | q | r | output
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 16: Logical gates
The smallest pieces of hardware that we will examine are called logical gates.
Every gate that we encounter will take bits as inputs and will emit one bit as output.
Those gates can connect to each other in various different ways in order to create more complex circuits
Gate

## Slide 17: Our first gate
0 | 1
1 | 0
0 | 1
1 | 0
This gate is known as the inverter.
It corresponds exactly to the negation operation in propositional logic!
  Where 1, set True.
  Where 0, set False
A
out

## Slide 18: Our second gate
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Corresponds to:
Conjunction
Disjunction

## Slide 19: Our second gate (AND gate)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Corresponds to:
Conjunction
Disjunction

## Slide 20: Our second gate (AND gate)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Corresponds to:
Conjunction
Disjunction

## Slide 21: Our third gate (OR gate)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Corresponds to logical disjunction (OR)

## Slide 22: Exercises
Which boolean function does this circuit correspond to?

## Slide 23: Exercises
Which boolean function does this circuit correspond to?

## Slide 24: Exercises
And this?

## Slide 25: Exercises
And this?

## Slide 26: And this?

## Slide 27: And this?

## Slide 28: And this?
Can we make this circuit cheaper?

## Slide 29: Simplifying the circuit…
New circuit: Three gates
Old circuit: Five gates

## Slide 30: Exercises
Which logical expression is computed by the following circuit?

## Slide 31: Exercises
Which logical expression is computed by the following circuit?
Simplify the circuit as much as possible!

## Slide 32: Coming back to our original formula…

## Slide 33: Coming back to our original formula…
For each small formula we have a circuit, and we will combine with a 4-input OR gate!

## Slide 34
For each small formula we have a circuit, and we will combine with a 4-input OR gate!
Circuit 1
Circuit 2
Circuit 3
Circuit 4
Coming back to our original formula…

## Slide 35: Circuit 1

## Slide 36: Circuit 2

## Slide 37: Circuit 3

## Slide 38: Circuit 4

## Slide 39: Midterm news / reminders
Panic-free midterm!
We will take an extra day or two to publish solutions
  In case somebody has had an emergency / ER / hospital visit / any other emergency.
  Monday: you will cover the midterm and have questions from today answered.
Today: Adder circuits!
  This concludes the logic portion!
Next week: Set Theory

## Slide 40: Midterm news / reminders
Next week: Set Theory and, possibly, quantifiers () on Thursday
  I will probably have you ensure on your own what and mean. Nothing more.
  Either textbook, or Wikipedia / Wolfram Alpha are good resources.
Remember: SpringBreak in two weeks.
  Next week’s homework will be designed for one week, but will have a 2-week deadline through 03-22.
  There will be a short quiz next week, which you will still have 1 week and 3 days to submit (Monday 03-22, 11:59pm, like your homework)
    But come on man, it’s a short quiz.

## Slide 41: Building Adder Circuits
We want to build circuits that add arbitrarily large binary numbers.
E.g
10011001
+00110011
11001100
Inputs
Output

## Slide 42: Half-Adder
A half-adder is a circuit that adds two bits together!
(Remember: is the carry bit.)
Let’s try to build a circuit that computes both S and C!

## Slide 43: Truth table
X | Y | S | C
0 | 0 | ? | ?
0 | 1 | ? | ?
1 | 0 | ? | ?
1 | 1 | ? | ?

## Slide 44: Truth table
X | Y | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 45: Truth table
X | Y | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
X
Y
C
S

## Slide 46: Truth table
X | Y | S | C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
X
Y
S
XOR Gate (“Exclusive OR)
X
Y
C
S

## Slide 47: Making XOR cheaper
First, let’s convince ourselves that

## Slide 48: Making XOR cheaper
First, let’s convince ourselves that

## Slide 49: Making XOR cheaper
First, let’s convince ourselves that

## Slide 50: Making XOR cheaper
First, let’s convince ourselves that
From five gates to four!

## Slide 51: Optimizing Half Adder
We can now optimize the Half Adder.
We won’t just use simplified XOR, but also leverage simplified XOR to re-use the AND gate used to compute the carry bit !

## Slide 52: Half Adder Abstraction
4 gates, instead of 6 for the previous one!

## Slide 53: Half Adder Abstraction
Half-Adder

## Slide 54: Full-Adder
Now, let’s consider the complete case, where we want to build a circuit that computes the sum of two 2-digit binary numbers:
To do this, we also need the ability to add 3 digits, because:
P Q
+ W X
C S1 S2
C1
P Q
+ W X
C S1 S2

## Slide 55: Full-Adder
Now, let’s consider the complete case, where we want to build a circuit that computes the sum of two 2-digit binary numbers:
To do this, we also need the ability to add 3 digits, because:
P Q
+ W X
C S1 S2
C1
P Q
+ W X
C S1 S2
We will call a circuit that adds 3 bits a full adder

## Slide 56: We could do the truth table….
P | Q | W | X | C | S1 | S2
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
P Q
+ W X
C S1 S2

## Slide 57: We could do the truth table….
P | Q | W | X | C | S1 | S2
0 | 0 | 0 | 0 |  |  | 
0 | 0 | 0 | 1 |  |  | 
0 | 0 | 1 | 0 |  |  | 
0 | 0 | 1 | 1 |  |  | 
0 | 1 | 0 | 0 |  |  | 
0 | 1 | 0 | 1 |  |  | 
0 | 1 | 1 | 0 |  |  | 
0 | 1 | 1 | 1 |  |  | 
1 | 0 | 0 | 0 |  |  | 
1 | 0 | 0 | 1 |  |  | 
1 | 0 | 1 | 0 |  |  | 
1 | 0 | 1 | 1 |  |  | 
1 | 1 | 0 | 0 |  |  | 
1 | 1 | 0 | 1 |  |  | 
1 | 1 | 1 | 0 |  |  | 
1 | 1 | 1 | 1 |  |  | 
P Q
+ W X
C S1 S2
But it’s time consuming and we are all busy people

## Slide 58: Constructing a Full-Adder in another way
We need to build a circuit that computes the sum of 3 digits, e.g P + Q + R
Step 1: Compute with a half-adder:
P
+ Q
C1S1
Half-Adder

## Slide 59: Constructing a Full Adder
Step 2: Compute with another half-adder:
Half-Adder
S1
+ R
C2S
Half-Adder
Half-Adder

## Slide 60: Constructing a full-adder
Step 3: Combine and with an OR gate to yield the final carry bit .
Half-Adder
Half-Adder

## Slide 61: Constructing a full-adder
Step 3: Combine and with an OR gate to yield the final carry bit .
Why did we choose an OR gate to combine the “intermediate” carries and ?
Half-Adder
Half-Adder

## Slide 62: Constructing a full-adder
Step 3: Combine and with an OR gate to yield the final carry bit .
Half-Adder
Half-Adder
Abstraction time!

## Slide 63: Full Adder Black Box
3 inputs, 2 outputs
Full Adder

## Slide 64: 2-bit adder
However, we still have not solved our original problem, which is to construct a circuit that adds 2-bit numbers!
So, we need a circuit that takes 4 inputs and emits 3 outputs:
P Q
+ W X
C S1 S2
2-bit adder

## Slide 65: Constructing a 2-bit adder
Step 1: Take care of the right-most column with a half-adder:
C1
P Q
+ W X
C S1 S2
Half-Adder

## Slide 66: Constructing a 2-bit adder
Step 1: Take care of the right-most column with a half-adder:
Step 2 (and final): Connect Half-Adder and new inputs to Full-adder appropriately to produce final circuit.
C1
P Q
+ W X
C S1 S2
Half-Adder
Full-Adder

## Slide 67: Constructing a 2-bit adder
Step 1: Take care of the right-most column with a half-adder:
Step 2 (and final): Connect Half-Adder and new inputs to Full-adder appropriately to produce final circuit.
C1
P Q
+ W X
C S1 S2
Half-Adder
Full-Adder
2-bit adder

## Slide 68: Constructing a 3-bit adder (messy)
C2 C1
A P Q
+ B W X
C3 S1S2 S3
Half-Adder
Full-Adder
Full-Adder

## Slide 69: Constructing a 3-bit adder (neat)
C2 C1
A P Q
+ B W X
C3 S1S2 S3
Full-Adder
2-bit adder

## Slide 70: Constructing an n-bit adder (messy)
HA
FA
We have full adders
How many XOR gates do we have?
FA
FA

## Slide 71: Constructing an n-bit adder (neat)
FA
(n-1)-bit adder

## Slide 72: Fun exercise
Input: number in binary (
Output (in : ???
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
Circuit

## Slide 73: Fun exercise
Input: number in binary (
Output (in : Binary to Unary converter!
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
Circuit

## Slide 74: First micro-circuit
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 75: Second micro-circuit
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 76: Second micro-circuit
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
(from distributive law of conjunction over disjunction!)

## Slide 77: Third micro-circuit
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 78: Third micro-circuit
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 79: Final circuit
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1

## Slide 80: Other numeric functions
Addition (have done)
Multiplication
Division
Primality test (test whether a number is prime)
There are circuits for all of these!
  Computers actually work this way at the base level: they consist of gates.